## Slide 1: ECE220 Lab2

## Slide 2: Brain Teaser – Right Shifting
Left shifting
  1101 1010
  ADD Rx, Rx, Rx
Right shifting
  1101 0110
  ?!?!
Solution
  Use two masks
  1101 0000
  1101 0010
  1101 0110

## Slide 3: MP2 – Stack Calculator
Implement a reverse Polish notation/postfix notation calculator
Notations:
Regular Notation
(3 – 4) + 5 = 4
3 – (4 + 5) = -6
Postfix Notation
3 4 – 5 + = 4
3 4 5 + - = -6
Standard notation requires parenthesis to reduce ambiguity whereas postfix doesn’t need any

## Slide 4: Stack Data Structure
xDE11
x5010
xFEE7
x57AB
xDEAD
xBEEF
Stack Memory
x5000
x4FFF
x4FFE
x4FFD
x4FFC
x4FFB
x4FFA
x4FF9
x4FF8
Stack End
Stack Top
Stack Start
Data Structure
  Add/remove elements from the top
  Stack of plates or stack of cards
  LIFO (Last In First Out) or FILO (First In Last Out)
  Operations
    POP – removes an element from the stack
    PUSH – pushes an element onto the stack
    SIZE – returns the size of the stack
    TOP – returns the element at the top of the stack

## Slide 5: Postfix Calculator on a Stack
Example input
  8 – (3 + 2) = 8 3 2 + - =
Algorithm
  PUSH when digit
  POP when operator, evaluate, PUSH result
  HALT on ‘=‘
Input
  8
  3
  2
  +
  -
  =
Stack Memory
x5000
x4FFF
x4FFE
x4FFD
x4FFC
x4FFB
x4FFA
x4FF9
x4FF8
Stack End
Stack Start
Stack Top
x0008
x0003
x0002
x0005
x0003

## Slide 6: Implementation
Read user input:
  GETC – Read a character from console into register R0 but don’t echo
  KBSR / KBDR – Status/display registers for keyboard
Echo user input:
  OUT – Write the character in register R0[7:0] to console
  DSR / DDR – Status/display registers for display
Subroutines
  JSR – saves contents of PC in register R7 and sets PC to new location
  RET – returns from a subroutine and replaces contents of PC with return address in register R7
  Save register values
    Caller vs callee saved registers
    SAVE_REGISTER .BLKW #1
    ST/LD instructions to save/load register values in subroutines

## Slide 7: Lab2 – Balancing Parentheses
Check if string of parentheses is balanced:
  Balanced
    ()()
    (())()
  Unbalanced
    )(
    ())
    (()
Output:
  Register R6 = x0001 (1) if balanced
  Register R6 = xFFFF (-1) if unbalanced
Algorithm
  Parse input from keyboard
    If input == ‘(‘, push to stack
    If input == ‘)’, pop from stack
    If input == ‘ ‘ (space), ignore it
    If input == ‘\n’ (xA) or ‘\r’ (xD)
      Check if stacks empty
      Halt

## Slide 8: Balancing Parentheses on a Stack
Input
  (
  (
  )
  )
x5000
x4FFF
x4FFE
x4FFD
x4FFC
x4FFB
x4FFA
x4FF9
x4FF8
Stack Memory
Stack End
Stack Start
(
(